## Slide 1: The 2014 Flash Flood and Intense Rainfall Experiment
Faye E. Barthold1,2, Thomas E. Workoff1,3, Wallace A. Hogsett1*, J.J. Gourley4, and David R. Novak1
With special thanks to Brian Cosgrove, NOAA/NWS/Office of Hydrologic Development
1NOAA/NWS/Weather Prediction Center, College Park, MD
2I.M. Systems Group, Inc., Rockville, MD
3Systems Research Group, Inc., Colorado Springs, CO
4NOAA/National Severe Storms Laboratory, Norman, OK
*Current Affiliation: Weather Analytics, Bethesda, MD

## Slide 2: Motivation
On average, flooding results in ~$8 billion
in damages and ~90 fatalities per year
7 of the last 10 NWS Service Assessments
have involved flooding
WPC Excessive Rainfall Outlooks
  Day 1-3 forecasts
  Highlight probability that rainfall will
  exceed flash flood guidance at a point
WPC Mesoscale Precipitation
Discussions
  Event-driven forecasts
  Highlight regions where heavy rainfall
  may lead to flash flooding in the next 1-6 hours

## Slide 3: Lessons Learned from 2013 FFaIR
High resolution convection-
allowing guidance can
provide valuable information
about the flash flood threat,
particularly when paired with
hydrologic information
Forecast verification extremely
difficult – no single
comprehensive source of
information about observed
flash flooding
?

## Slide 4: Flash Flood and Intense Rainfall Experiment July 7-25, 2014
23 participants representing operations,
research, and academia
Daily Activities
  18 hr CONUS probabilistic flash flood
  outlook (18-12 UTC)
    Prototype of next generation ERO
  6 hr event-driven probabilistic flash flood
  forecasts (18-00 UTC and 00-06 UTC)
  Forecast discussion
    Used to brief concurrent HWT-Hydro
    experiment
  Subjective evaluation
Explore the utility of convection-allowing models in the flash flood forecast process

## Slide 5: Featured Model Guidance
Provider | Model | Resolution | Forecast Hours
EMC | Parallel NAM* | 12km (parent) 4km (nest) | 84 (parent) 60 (nest)
ESRL/GSD | HRRR | 3 km | 15
SPC | SSEO (7 members) | 4 km | 36
WPC | Modified SSEO (7 members) | 4 km | 24
EMC | NCASE-TL (15 members) | 4 km | 12
ESRL/GSD | ExREF (8 members) | 9 km | 84
*The parallel NAM used during the experiment became operational on 12 August 2014
Parallel NAM
HRRR
SSEO
Modified SSEO
NCASE-TL
ExREF

## Slide 6: Ensemble Forecast Tools Neighborhood Probabilities
Probability of an event occurring within a certain distance of a grid point
  40 km radius
Accounts for spatial uncertainty in the forecast
1.4”
2.4”
.78”
2.3”
2.7”
3.7”
2.8”
4.3”
1.8”


















Is QPF > 2”?
Max member QPF

## Slide 7: Ensemble Forecast Tools Neighborhood Probabilities
Events
  Probability of QPF exceeding a threshold (e.g. 3”)
  Probability of QPF exceeding FFG
  Probability of QPF exceeding % FFG
QPF > FFG
QPF > 90% FFG
QPF > 75% FFG

## Slide 8: Flash Flood Verification Database
WPC flash flood verification database
  NWS Local Storm Reports
    Flash flood
    Flood
  NSSL mPING reports of flooding
  USGS stream gauge exceedance
  information
Postgres database updated
throughout the day to capture
latest observations
Can request data for user-defined
time periods
Yellow – flash flood LSR
Blue – flood LSR
Brown – mPING
Pink - USGS

## Slide 9: “Practically Perfect” Analysis Technique
Converts point observations
into contoured probabilistic
forecast areas using a Gaussian
weighted function
Work in progress
  Consider including additional data
    Heavy rain LSRs
    Flash flood warnings
    QPE
  Consider weighting datasets
  differently based on quality of data
  source and relevance to flash flooding

## Slide 10: Experiment Findings
The NWS needs to have a more consistent approach to the flash flood problem from definition, to warning practices, to reporting
  Inconsistencies from WFO to WFO result in a moving target when trying to identify where flash flooding has occurred
Convection-allowing ensembles are invaluable to the flash flood forecast process, especially when paired with hydrologic data in the form of neighborhood probabilities
  Helps account for spatial uncertainty in both QPF and the hydrologic response

## Slide 11: Experiment Findings
Flash flood forecasting in the western U.S. represents a more significant challenge
  Need both improved model guidance and improved forecaster understanding of the unique drivers of flash flooding in the west
Updating WPC’s Excessive Rainfall Outlook to use a neighborhood probabilistic approach will provide more inclusive forecast guidance highlighting the threat for flash flooding

## Slide 12: Future Work
Explore alternative hydrologic information for neighborhood probabilities
  Precipitation recurrence intervals
Make neighborhood probabilities of QPF > FFG available via FTP
Continue to explore improved flash flood forecast verification
  Refine practically perfect technique
  Make verification database publically accessible
Full experiment report available at:
http://www.hpc.ncep.noaa.gov/hmt/FFaIR_2014_final_report.pdf